## Slide 1: WRM200 Dual Polarization Weather Radars for Met. Service, System Block Diagram
January 2020

## Slide 2: WRM200 Dual Polarization Doppler Weather Radar Site
Radome
for Antenna and Pedestal
Radar Room
TCP/IC
Met. Service Radar Center
Pedestal
WRP221
Dual
Polarization
Antenna
WRA111
Pedestal
Protection
Unit (PPU)
Main
Distribution
Unit (MDU)
Battery
Backup
Unit (BBU)
Uninterrupted
Power
Supply (UPS)
8 kVA
Radar Station
WRM200 Dual Pol. Radar Cabinet with
RVP902 Server and
IRIS/Radar sw
AC Power Input
230/400 VAC, 50Hz
3-phases, 5-wires
Waveguides
Antenna filters,
harmonic & bandpass
RAW Polar
Data Out
(TCP/IP)
≥ 2 Mbps
Servers and Workstations
Ave. 2100 W

## Slide 3: Central Site Configuration
Met. Service in Podgorica
HP
L2245w
IRIS Analysis and IRIS Focus Web servers for product generation and display
HP
L2245w
Optional remote IRIS users. Accessing IRIS Focus software remotely
Internet
IRIS Focus workstations
5 User Seats (licenses)
HP
L2245w
Network data communication (https)
Vrsuta
Other optional data sources (e.g. Lightning data, rain gauge data)
Network data communication (TCP/IP)
Native IRIS data or ODIM HDF5
New Vaisala C-band
Weather Radar
Ethernet
GB switch

## Slide 4: Weather Radar Tower and Equipment Shelter
Tower, 15 m
Shelter
Complete system

## Slide 5
Foundation design for 15 m tower, for wind up to 60 m/s Size 8.3 m x 8.3 m x 1.2 m
Pos | Reinforcement (A500HW) | Shape | Weight
1 | 147 pcs, Φ16 mm, tot. 1203 m | 818 cm | 1900 kg
2 | 14 pcs, Φ8 mm, tot. 115 m | 818 cm | 70 kg
3 | 6 pcs, Φ8 mm, tot. 95 m | 591 cm x 591 cm | 60 kg
4 | 148 pcs, Φ25 mm, tot. 205 m | 32 cm + 106 cm | 800 kg
Tower Foundation – main features:
size 8.3 x 8.3 x 01.2 m3, volume 83 m3, weight 150 tn
reinforced concrete C30/37 (see the table below)
Formwork totally 30 m2

## Slide 6: Budgetary Pricing
Budgetary Pricing for one WRM200 and Central System with Services in k€ without tax
WRM200 Radar System with 1 year site warranty 765
Freight 10
Radome with accessories 80
IRIS Radar software 50
Radar System Factory Acceptance Tests, 3 days 5
Installation supervision by Vaisala, totally 20 days 30
Radar Site Acceptance Tests, 3 days 3
IRIS Focus & Analysis software, 5 seats 50
Central Site server(s) 6
Workstations with browsers, 5 pcs 5
Central Site installation, 4 days 6
Training at factory, Finland, 10 days 15
Training at site, 5 days 7.5
Training for Central System, 5 days 7.5
Five (5) years spare part set 50
Set of Test Equipment and Tools 40
TOTAL in EUR: 1100 k€
Optional extended warranty, price per year, incl.: 28
Preventive and repair maintenance at site
Express spare part delivery
Spare parts
Priority technical support
Local Site Works
Rent of cranes and lifting equipment 5
Installation / construction man force locally 20
Electricity and grounding installations at the site 10
Steel tower, 15 m high 100
Excavation works + materials 20
Tower concrete foundation, 8.3m x 8.3m x 1.2m, totally 83 m3 25
Radar equipment shelter 10
Air conditioning for radar shelter and radome 10
Back up diesel generator with shelter and installation 30
Site fencing and security 10
TOTAL in EUR: 240 k€